## Slide 1: Stereo Visual Odometry
Chirayu Garg
Utkarsh jain

## Slide 2: What is Visual Odometry?
Visual Odometry is the estimating the motion of a camera in real time using sequential images
The idea was first introduced for planetary rovers operating on Mars – Moravec 1980
6-DOF of the robot
  Euler Angles
  Cartesian Coordinates

## Slide 3: VSLAM
Simultaneous Localization and Mapping
The goal of SLAM is to obtain a global, consistent estimate of the camera's path
Visual Odometry is used as a building block of SLAM
SLAM finds loop closures in the paths generated by Visual Odometry and adjusts the drifts in the path

## Slide 4: Applications of Visual Odometry
Movement prediction in uneven terrains
Motion estimation for vehicles
  HD mapping
  Autonomous cars
Possible use in AR/VR applications
Challenges
  Robustness to lighting conditions
  Lack of features / non-overlapping images
  Without loop closure the estimate still drifts
Notes: Contrary to wheel odometry, Visual Odometry is not affected by wheel slip in uneven terrain or other adverse conditions.

## Slide 5: Types of Visual Odometry
Stereo Visual Odometry
Solves the scale problem
Feature depth between images
Degenerates to the monocular case if only distant features are used
Monocular Visual Odometry
A single camera = angle sensor
Motion scale is unobservable (it must be synthesized)
Best used in hybrid methods

## Slide 6: Augmented Stereo Visual Odometry
Lidar
Time-of-flight
RGB-Depth
GPS
*Image - https://www.wired.com/2015/04/cost-of-sensors-autonomous-cars/

## Slide 7: The Dataset
KITTI Vision Benchmark Suite dataset by KIT, Germany
Grayscale and color image data, with LIDAR laser data
  Undistorted and stereo rectified
  W x H – 1241 x 376
Calibration camera projection matrices are provided
The output poses for each frame are with respect to the 0th image in the sequence
Notes: Stereo rectification: Apply projective transformation so that epipolar lines correspond to horizontal scanlines

## Slide 8: Algorithm
Real-Time Stereo Visual Odometry for Autonomous Ground Vehicles by Andrew Howard, IEEE 2008
Image Sequence
Feature Detection
Feature Matching
3D point cloud generation
Inlier Detection
Motion Estimation

## Slide 9: Feature Detection
FAST (Features from Accelerated Segment Test) corner detection
  Feature Bucketing
Disparity computation from Stereo images

## Slide 10: Feature Matching
KLT Tracker is used to find corresponding feature points at T+1
  Search Window – 15x15
  Pyramid Level – 3
Feature points pruning
Notes: KLT tracker is used for finding corresponding points, instead of feature descriptor computation for both images and comparing features for matching
Point pruning – KLT rejected, KLT error, out of target bounds

## Slide 11: 3D Point Triangulation
Corresponding feature points (u,v) from left and right image
Disparity displaced right image coordinate
=
Least square minimization on system of equations for , solved using SVD

## Slide 12: Inlier detection
Clique building on consistent 3D points with same distance at time T and T+1
Grow clique with connected points
i
j
i
j
d
d
T
T+1

## Slide 13: Motion Estimation
Minimize image re-projection error
  Levenberg-Marquardt least squares estimation
  ja, jb – 2D image coordinates
  wa, wb – 3D world coordinates
  Δ - 4x4 Transform Matrix
  P – 3x4 Projection Matrix
ja
jb
Δ
Wa
Wb
T
T+1

## Slide 14
Demo

## Slide 15: Results
Ground Truth
SVO
Seq 00
Seq 02

## Slide 16: Results: FAST vs SIFT
Ground Truth
SVO
FAST
SIFT
Seq 02
Seq 02

## Slide 17: Results: Clique vs RANSAC
Ground Truth
SVO
FAST
SIFT
Seq 00
Clique
Seq 00
RANSAC

## Slide 18: Tunable Parameters
Disparity computation – block size, number of disparities
KLT tracker – block size, image scale (pyramid)
  KLT error threshold
Clique consistent point difference threshold
Re-projection error threshold

## Slide 19: Future Work
Brightness invariant feature tracking
  Neural network for feature matching - Universal Correspondence Network
Faster inlier detection
Integration of other sensor data

## Slide 20: References
[1] A. Howard. Real-time stereo visual odometry for autonomous ground vehicles. In IEEE Int.
Conf. on Intelligent Robots and Systems , Sep 2008
[2] C. B. Choy, J. Gwak, S. Savarese and M. Chandraker. Universal Correspondence Network.
NIPS , 2016
[3] http://www.cvlibs.net/datasets/kitti/eval_odometry.php